## Slide 1
Week 12 Recitation
Op-Amp & Review
Rifat Bin Rashid
Teaching Assistant
Dept. of ECE, Rutgers University

## Slide 2
 | Q1 | Q0 | X | D1 | D0 | R | G | B
 | 0 | 0 | 0 |  |  |  |  | 
 | 0 | 0 | 1 |  |  |  |  | 
 | 0 | 1 | 0 |  |  |  |  | 
 | 0 | 1 | 1 |  |  |  |  | 
 | 1 | 1 | 0 |  |  |  |  | 
 | 1 | 1 | 1 |  |  |  |  | 
 | 1 | 0 | 0 |  |  |  |  | 
 | 1 | 0 | 1 |  |  |  |  | 
(20 points) Examine the following schematic. Label each AND gate with the term it computes (ex. Q1’Q0X’) Then fill in the equation of each variable. Then complete the truth table D1 = ___________________________ D0 = ___________________________ R = ____________________________ G = ____________________________ B = ____________________________

## Slide 3
 | Q1 | Q0 | X | D1 | D0 | R | G | B
 | 0 | 0 | 0 |  |  |  |  | 
 | 0 | 0 | 1 |  |  |  |  | 
 | 0 | 1 | 0 |  |  |  |  | 
 | 0 | 1 | 1 |  |  |  |  | 
 | 1 | 1 | 0 |  |  |  |  | 
 | 1 | 1 | 1 |  |  |  |  | 
 | 1 | 0 | 0 |  |  |  |  | 
 | 1 | 0 | 1 |  |  |  |  | 
(20 points) Examine the following schematic. Label each AND gate with the term it computes (ex. Q1’Q0X’) Then fill in the equation of each variable. Then complete the truth table D1 = ___________________________ D0 = ___________________________ R = ____________________________ G = ____________________________ B = ____________________________

## Slide 4
X (Input) | Q1 (Current State) | Q0 (Current State) | D1 (Next Q1) | D0 (Next Q0)
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 5
(10 points) Complete the state machine based on the truth table above.

## Slide 6: Timing Hazard
AB \ CD | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 0 | 0
11 | 1 | 1 | 1 | 1
10 | 1 | 0 | 1 | 1
AC + CD + B’C
Adjacent 1’s should belong to the same group/chain.

## Slide 7: Operational Amplifiers

## Slide 8: Operational Amplifiers
Key Characteristics:
Differential Inputs: Two inputs, one non-inverting (+) and one inverting (-).
High Gain: Amplifies the voltage difference between inputs by a huge factor (e.g., 10,000+).
High Input Impedance: Draws very little current from the input signals.
Low Output Impedance: Can supply current to the output with minimal voltage loss.
Single-Ended Output: Produces one output voltage.

## Slide 9: Operational Amplifiers
How It Works:
The output voltage Vout is approximately the gain (A) times the voltage difference between the inputs Vin+ and Vin-
              Vout=A (Vin+-Vin-)
In negative feedback (most common), the op-amp adjusts its output to try and make the voltage at the inverting input equal to the non-inverting input, simplifying analysis.
Common Applications:
Amplifiers: Inverting, non-inverting, differential.
Comparators: Comparing two voltages.
Filters: Active filters for frequency selection.
Signal Conditioning: Amplifying sensor signals, noise reduction.
Mathematical Functions: Summing, subtracting, integrating, differentiating.

## Slide 10: Operational Amplifiers