## Slide 1
Week 5 Recitation
Verilog & K Map
Rifat Bin Rashid
Teaching Assistant
Dept. of ECE, Rutgers University

## Slide 2: K Map
Minterms --- SOP --- Collect/Place 1
Maxterms --- POS --- Collect/Place 0
A | B | minterm | maxterm
0 | 0 | A’B’ | A+B
0 | 1 | A’B | A+B’
1 | 0 | AB’ | A’+B
1 | 1 | AB | A’+B’

## Slide 3
F(A, B, C, D) = (A’ + B’ + D’)(A + B’ + C’)(A’ + B + D’) (B + C’ + D’)
 | 00 | 01 | 11 | 10
00 |  |  |  | 
01 |  |  |  | 
11 |  |  |  | 
10 |  |  |  | 
AB
CD
A+B
A+B’
A’+B’
A’+B
C+D
C+D’
C’+D’
C’+D

## Slide 4
F(A, B, C, D) = (A’ + B’ + D’)(A + B’ + C’)(A’ + B + D’) (B + C’ + D’)
 | 00 | 01 | 11 | 10
00 |  |  | 0 | 
01 |  |  | 0 | 0
11 |  | 0 | 0 | 
10 |  | 0 | 0 | 
AB
CD
A+B
A+B’
A’+B’
A’+B
C+D
C+D’
C’+D’
C’+D

## Slide 5: 4-state logic
In Verilog/SystemVerilog simulation, signals use 4-state logic:
    0 = logic low
    1 = logic high
    x = unknown (value can’t be determined)
    z = high-impedance (not being driven)

## Slide 6: Verilog Procedural blocks
Two types.
initial block:
    This block executes only once at the beginning of a simulation (time 0) and is non-synthesizable, meaning it cannot be converted into actual hardware. It is typically used in testbenches for initial value setup.
            initial begin
            // statements
            end
always block:
    This block continuously executes statements based on a sensitivity list.
            always begin
            // statements
            end

## Slide 7
`timescale 1ns/1ns
module my_tb;
logic [3:0] a = 4'b1001;
logic [3:0] b;
initial begin
logic [3:0] result = a & b; // a AND b
$display("%b", result);
result = a | b; // a OR b
$display("%b", result);
result = a ^ b; // a XOR b
$display("%b", result);
b = { ~a[3:2], a[1:0] }; // b = 01_01 when a=1001
result = ~(a & b); // a NAND b
$display("%b", result);
end
endmodule
Question 1:

## Slide 8
`timescale 1ns/1ns
module my_tb;
logic [3:0] a = 4'b1001;
logic [3:0] b; // b is not assigned , so b= xxxx
initial begin
logic [3:0] result = a & b; // a AND b
$display("%b", result);
result = a | b; // a OR b
$display("%b", result);
result = a ^ b; // a XOR b
$display("%b", result);
b = { ~a[3:2], a[1:0] }; // b = 01_01 when a=1001
result = ~(a & b); // a NAND b
$display("%b", result);
end
endmodule
Result:
x00x
1xx1
xxxx
1110
Solution 1:

## Slide 9: Timescale 1ns/1ns
timeunit 1ns;
timeprecision 1ns;

## Slide 10
Complete the following system Verilog program. The timescale should be 2ns, splitting each delay in 100 parts to look for timing hazards.
`timescale ________________ _________ ALU_8bit_tb; _____ [7:0] a; _____ [7:0] b; initial _______ a = 15; b = 23; reg[7:0] c = a & b; // c = __________ reg[7:0] d = a | b; // d = __________ reg[7:0] e = a ^ b; // e = __________ reg[7:0] f = a << 2; // f = _________ reg[7:0] g = b >> 1; // g = _________ reg[7:0] h = {a[0],a[7:1]};// h = _________ _____ // set a delay so this program ends after 1μs (1000ns) $finish; end forever begin ________ clk = _________clk; // set timing so clock has period of 4ns end _________
Question 2:

## Slide 11
`timescale 2ns/20ps
module ALU_8bit_tb;
reg [7:0] a;
reg [7:0] b;
initial begin
a = 8'd15; // 0000_1111
b = 8'd23; // 0001_0111
reg [7:0] c = a & b; // c = 8'b00000111
reg [7:0] d = a | b; // d = 8'b00011111
reg [7:0] e = a ^ b; // e = 8'b00011000
reg [7:0] f = a << 2; // f = 8'b00111100
reg [7:0] g = b >> 1; // g = 8'b00001011
reg [7:0] h = {a[0], a[7:1]};// h = 8'b10000111
#500; // stop after 1 μs (1000 ns)
$finish;
end
// Clock with 4 ns period (2 ns high + 2 ns low)
forever begin
#1;
clk = ~clk; // toggle every 2 ns (timescale unit)
end
endmodule
Solution 2:

## Slide 12
Test 1
Next Wednesday – October 15
Time: 12:10 Pm -1:30 Pm
Place: SEC-209
For Recitation section 02