## Slide 1
Week 4 Recitation
K Map
Rifat Bin Rashid
Teaching Assistant
Dept. of ECE, Rutgers University

## Slide 2: K MAP
❖ A systematic way of producing a minimum-cost logic expression
K-map provides the minimized SOP or POS version (not the most minimized form)

## Slide 3: K-Map: Main Idea
If a bit changes, it does not matter. If it stays the same, it matters
A | B | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
SOP: f = AB’ + AB
= A( B’+B)
=A
POS: f = (A+B)(A+B’)
= A+ AB’ + AB+ BB’
=A
 | 0 | 1
0 | m0 | m1
1 | m2 | m3
A
B
 | 0 | 1
0 | 0 | 0
1 | 1 | 1
A
B

## Slide 4: K-Map: Main Idea
❖1s for SOP, 0s for POS
❖Terms- minterm format for SOP, maxterm format for POS
A | B | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
SOP: f = A’ + B
POS: f = A’ + B
 | 0 | 1
0 | m0 | m1
1 | m2 | m3
A
B
 | 0 | 1
0 | 1 | 1
1 | 0 | 1
A
B

## Slide 5: Two steps
Create the K map
(from truth table / Boolean function/ Given)
2. Minimize using the k map
(Minimized SOP / POS)

## Slide 6
K Map Minimization Rules:
K-map provides the minimized SOP or POS version (not the most minimized form)
If a bit changes, it does not matter. If it stays the same, it matters
Include all 1’s for SOP and all 0’s for POS. Minterm format for SOP, maxterm format for POS

## Slide 7
K Map Minimization Rules:
Select the largest chain (lateral or vertical) or rectangle with size 2𝑛 where
n=0,1,2,3,… (even if some part of the largest is already selected)
Number of variables in a term = Total number of variables – n
Chains may partially overlap (but full overlap is redundant)
Grey coding is cyclic. So, the ends are connected
Practice! Practice!! Practice!!!

## Slide 8: Three Variable
 | 00 | 01 | 11 | 10
0 | m0 | m1 | m3 | m2
1 | m4 | m5 | m7 | m6
A
BC

## Slide 9: Three Variable
A | B | C | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1
A
BC

## Slide 10: Three Variable
A | B | C | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1
A
BC
AC'+B'C

## Slide 11: Four Variable
 | 00 | 01 | 11 | 10
00 | m0 | m1 | m3 | m2
01 | m4 | m5 | m7 | m6
11 | m12 | m13 | m15 | m14
10 | m8 | m9 | m11 | m10
AB
CD

## Slide 12: Four Variable Example 1
 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 1 | 1
11 | 1 | 0 | 0 | 1
10 | 1 | 0 | 0 | 1
AB
CD

## Slide 13: Four Variable Example 1 (continued)
 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 1 | 1
11 | 1 | 0 | 0 | 1
10 | 1 | 0 | 0 | 1
AB
CD
A'BC+AD'

## Slide 14: Four Variable Example 2
 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 1 | 1
11 | 1 | 1 | 1 | 1
10 | 1 | 1 | 1 | 1
AB
CD

## Slide 15: Four Variable Example 2 (continued)
 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 1 | 1
11 | 1 | 1 | 1 | 1
10 | 1 | 1 | 1 | 1
AB
CD
A+BC

## Slide 16: Four Variable Example 3
 | 00 | 01 | 11 | 10
00 | 1 | 1 | 1 | 0
01 | 1 | 1 | 1 | 0
11 | 0 | 0 | 1 | 1
10 | 0 | 0 | 1 | 1
AB
CD

## Slide 17: Four Variable Example 4
 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 1 | 1 | 0
11 | 1 | 1 | 0 | 1
10 | 1 | 1 | 1 | 1
AB
CD

## Slide 18: Four Variable Example 5
 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 1 | 1 | 1 | 0
11 | 1 | 1 | 1 | 0
10 | 0 | 1 | 0 | 0
AB
CD

## Slide 19: Four Variable Example 6
 | 00 | 01 | 11 | 10
00 |  |  |  | 
01 |  | 1 | 1 | 
11 | 1 | 1 |  | 1
10 | 1 | 1 | 1 | 1
AB
CD

## Slide 20: Four Variable Example 6 (continued)
 | 00 | 01 | 11 | 10
00 |  |  |  | 
01 |  | 1 | 1 | 
11 | 1 | 1 |  | 1
10 | 1 | 1 | 1 | 1
AB
CD
A'BD+AB'+AD’ + AC’

## Slide 21: Four Variable Example 7
 | 00 | 01 | 11 | 10
00 | 1 | 1 |  | 
01 |  | 1 | 1 | 
11 |  |  | 1 | 1
10 | 1 |  |  | 1
AB
CD

## Slide 22
If a bit changes, it does not matter. If it stays the same, it matters.